Main malfunction and solving ways of mosquito mat packing machine

| Malfunction type | Phenomenon & solving way |
| --- | --- |
| Machine stop suddenly Motor can not started | Do not start the machine anxiously, first open the electric box, to see the overloading protector slips, if yes, to be safe, turn off the power, turn the motor main shaft with hand, turn at least one cycle, if it is very easy to do so, maybe the motor is over-heated, then wait until the motor temperature is down and start the machine again; if the machine is overloaded, then check the reason which causes the overload in three steps: first open the clutch of the mats-impulse device, then it is easy to find out whether the cutting device and heating roller are overloading or not, then close the clutch of the mats-impulse device, open the clutch of liquid medicine impulse device, then could check whether it is problem of the medicine-impulse system, finally close the liquid-impulse device, then could check the liquid-impulse system, if the fuse wire of the motor is burned, then replace a new one The motor connector are not well connected, which lack of phase Lack of phase for electric power supply, check the connecting status of the plugs and socket It is normal phenomena that the mats are stucked |
| Motor running normally, but the power output are too small | Mainly the friction clutch on the output shaft of the speed-decreasing box are too loose, please use spanner to fasten it Oil enters into the friction clutch on the output shaft of the speed-decreasing box, which causes skid bye the oil, please clean-up the oil The setting of the frequency convertor is not logical, please set again according to the user manual of the frequency convertor |
| Mats pusher get stuck | Rotate the motor in inverted direction, exit the pusher, take out the sticking mats |
| Bubbles appear in the liquid medicine, the medicine flow back or out | The tubes are air-leaked, fasten the joint and make it air-proof One-way valves are stuck, clean the valve and pump with kerosene Sealing washer are broken, change the piston and sealing washer in the pump |
| When adjust the kinetic length of the piston pole during production, when it is much longer than others | It is clear that there is precipitate or dreg in the pump, please clean out with kerosene in time |
| Fuzz appears when feed the mats | The mats are too thick, check the thickness Please adjust when the mat-pusher are moved The impulse panel are bent, please change or rectify |
| The heat-seal roller press the mats during product | Mats are too thin The machine are not stable, with too much shake, please adjust Tooth gap is too large, please adjust The bearing of the to-and-fro organ for the mat-impulse are damaged, please replace |
| The change of the cutting position are too big | The brake of the aluminum foil roller are too tight, adjust the brake The edge of the aluminum foil surface is not tightly pressed When the diameter of the aluminum foil roll is comparatively small caused by consumption, the brake pressure will become bigger, adjust it The teeth-gap of the cutting transmission system are too big, please adjust it The driving device is not well connected, please adjust it |
| Products with wrinkle | The strength from upper and lower are not even, please adjust the brake strength |
| Products get shorter | The brake strength is too big, |
| Not well heat-sealed | The roller’s press strength is not even Quality problem of aluminum foil, change it Temperature too low, reset the temperature Carbon brushes of the roller are not well connected |
| The temperature rising time of the roller is too long, temp-control is not good | The head of the thermocouple is not well connected to the roller, reconnect it |
| Traction crinkle | The position between the rubber driving wheel and the driving roller are deflected, readjust it |
| The foil stick seriously to the roller | Temperature too high, speed too slow, make the temperature lower or make the speed fast The sticking material on the roller is not cleaned timely Spread a layer of silicon oil on the roller with brush |
| The liquid medicine is not round-injected or in line or some big drop lugged with several small drops | Adjust the relative angle of the medicine impulse protruding wheel(cam), Speed is higher than 630pc/min. make it lower |
| Linkage problem cutting | Position fault or too much distance with the two pairs of scissors, which need to be adjusted, detailed as drawing |